UN-BOXXaero+ - antistatic bin for disposal of empty or partially empty aerosols, even if there are special safety requirements

With the UN-BOXXaero+, P. HENKEL GmbH is now offering a bin to dispose of empty or partially empty aerosols with antistatic properties. The bin is UN-certified and permitted for UN 1950 (the legal requirement to collect empty and partially empty aerosol cans). Thanks to the special surface resistance of 10 to the power of 9, the bin is permanently antistatic, thereby significantly reducing the risk of a sudden discharge. The UN-BOXXaero+ is therefore ideal for disposing of aerosols with special safety requirements, as is often mandatory in industrial buildings. The collection bin is equipped with ventilation openings that allow good air circulation and ventilation, which is also necessary from a safety point of view. You also have the option of choosing a lid with an opening for filling. For safety reasons, a means of absorbing free liquids is required as additional equipment. Thanks to the large wheels on the UN-BOXXaero+, it can be easily moved to where it is needed. Different colours and an individual print design are available depending on the quantity ordered. The bin has a volume of approximately 120 L.